LB(T)-800-61

Powerful pumps built with durable materials in an easy handling design.

Top discharge provides maximum motor cooling efficiency allowing continuous duty operation at low water levels and extended dry-run capability.

FEATURES

            - Designed to fit an 8’’ pipe.

            - Up to 60’ shut off head

            - Double inside Mechanical Seal with SiC

            - Oil filter provides lubrication of the seal faces.

            - 50’ Cable Length

            - Maximum Capacity 73GPM

Optional accessories

            - TS-302 Float Switch for automatic operation

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals–Sales–Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100

| Model | LB(T)-800 |
| --- | --- |
| Max. Capacity (GPM) | 73 |
| Max. Head (ft) | 59 |
| Discharge Connection (in) | 2” |
| Motor Output | 1hp |
| Voltage (V) | 110V |
| Amperage – rated current | 10.1 |
| Amperage – starting current | 40.4 |
| Std. Cable length (ft) | 50 |
| Max. Cable Length (ft) | 55 |
| Min. Generator Capacity (watts) | 3300 |
| Max. Diameter (in.) | 7 ½ |
| Max. Height (in.) | 13 7/16 |
| Continuous Running water level (in.) | 2” |
| Pump Weight | 35 lbs |

| Tether length | Pumping range |
| --- | --- |
| 3.5 (in) | 7 (in) |
| 6 (in) | 10 (in) |
| 10 (in) | 16 (in) |
| 14 (in) | 22 (in) |
| 18 (in) | 28 (in) |
| 22 (in) | 33 (in) |
| 24 (in) | 36 (in) |
| Note: Due to weight of cable, pumping range above horizontal is NOT equal to pumping range below horizontal. As tether length increases, so does the variance of the pumping range. Pumping ranges are based on testing in non-turbulent conditions. Actual conditions may vary. |

Float Switch Range

Tsurumi’s new design features an angled casing and discharge connector. The unique slotted design of the discharge connectors bolt holes, provides for quick conversion from vertical to horizontal discharge configuration. This allows the end use to configure the LB-800 to the installation, thereby providing for more stable operation and at the same time reducing kinking of the discharge hose

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals–Sales–Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100