LB-480(A)-62

Powerful pumps built with durable materials in an easy handling design.

Model LB-480A Automatic Submersible Pump performs like the non-automatic version in every aspect of construction site usage requiring a tough and durable pump.

FEATURES

            - No control panel or float switches required.

            - Performs like the non-automatic pump with no special float installation required.

            - Requires very small space to operate – only 8 ¾’’ diameters.

            - Urethan, Semi Vortex Impeller and wear plates for maximum durability with maintaining pump performance.

            - Double inside Mechanical Seal With SiC faces provides for maximum life.

            - Oil lifter provides lubrication of the seal faces. (patent pending)

            - V-Ring Seal Protector designs mechanical seal from abrasive particles.

            - Environmentally friendly, reducing electrical costs and operational noise.

Technical features of EL-1 Relay UniT

            - Sensitive electrodes detect water to start pump operation even when foreign materials are present.

            - Internal timer eliminates frequent on/off operation in rough water to extend motor life.

            - Relay sensor completely molded in resin and covered by rubber case for protection against rough handling.

            - Jobsite tested for more than 30,000 on-off cycles without failure or damage.

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals–Sales–Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100

| Model | LB-480(A)-62 |
| --- | --- |
| Max. Capacity (GPM) | 62.4 |
| Max. Head (ft) | 39.5 |
| Discharge Connection (in) | 2” |
| Motor Output | 2/3 hp |
| Voltage (V) | 110V |
| Amperage – rated current | 6.1 |
| Amperage – starting current | 12.5 |
| Std. Cable length (ft) | 32’ |
| Max. Cable Length (ft) | 62’ |
| Min. Generator Capacity (watts) | 1300 |
| Max. Diameter (in.) | 8 ¾ |
| Max. Height (in.) | 11 3/16 |
| Continuous Running water level (in.) | 4 ½’’ |
| Pump Weight | 30 lbs |

| Electrodes submerged in water closing circuit for electric current. The pump starts to operate | Water level has fallen Electrodes in air opening circuit for electric current. Timer starts and pump continues to operate | Time continues pump operation for approximately one minute, If water again contacts, the electrodes timer is cancelled and pump continues operating. | Timer stops after approximately one minute. | Water level rises to contact electrodes and the pump restarts |
| --- | --- | --- | --- | --- |
| Pump begins operating. Water level falls | Pump continues operating. Water level falls | Pump continues operating. Water level falls | Pump stops. Water level rises. | Pump begins operating. Water level falls. |

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals–Sales–Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100