NK2-15

Heavy duty high head pumps capable of handling abrasive materials with minimal wear

Heavy duty, high head single-phase pumps available in 110v or 220v. Optional agitator kits allow continuous duty when pumping abrasive materials.

FEATURES

            - Terminal board for voltage reconnect allows for change from 110V to 220V

            - Semi Vortex Impeller and Synthetic Rubber Wear Plates for maximum durability and maintaining pump performance

            - Double inside Mechanical Seal with SiC faces provides the longest operational life

            - Oil filter provides lubrication of the seal faces. (patent pending)

            - V-Ring seal design protects mechanical seal from abrasive particles

            - Maximum Capacity 111GPM

            - Available in 110V & 220V

Optional accessories

            - TS-303 Float Switch for automatic operation

            - Sand Kit to suspend solids and prevent clogging.

            - 2-inch NPT coupling acailable

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals – Sales  –Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100

| Model | NK2-15 |
| --- | --- |
| Max. Capacity (GPM) | 111 |
| Max. Head (ft) | 69 |
| Discharge Connection (in) | 3” |
| Motor Output | 2hp |
| Voltage (V) | 110V or 220V |
| Amperage – rated current | 23.0(110V) 11.5(220V) |
| Amperage – starting current | 136(110V) 68(220V) |
| Std. Cable length (ft) | 32 |
| Max. Cable Length (ft) | 46(110V) 185(220V) |
| Min. Generator Capacity (watts) | 6000 |
| Max. Diameter (in.) | 9 7/16 |
| Max. Height (in.) | 24 ½ |
| Continuous Running water level (in.) | 3 ¼ |
| Pump Weight | 81 lbs |

# Sand Kit

Turn your NK Series dewatering pump into a sand/aggregate pump with the addition of our sand kit to your order. Our sand kit helps suspend the sand and solids that you sometimes encounter on what should have been a routine dewatering application.

ATS EQUIPMENT INC. 	Construction Equipment & Supplies	Rentals – Sales  –Service

BOSTON, MA 	AUBURN, MA 	SEEKONK, MA 	CANDIA, NH

(617) 825-3600 	(508) 832-8500	(508) 379-6200	(603) 483-2100